## Slide 1
Check mode
TURN OFF LAMP INDICATOR
2
TURN ON LAMP INDICATOR
HIGH TEMP
high_temp_sec ++
normal_temp_sec=0
NORMAL TEMP
normal_temp_sec ++
high_temp_sec=0
normal_temp_sec == 30
high_temp_sec == 30
Temperature sensor
One time per second
One time per second
K-15
temp_cel
> 120°C
NO
YES
temp_cel
<= 120°C
NO
YES
LAMP
OFF
YES
NO

## Slide 2
temp_cel | Output from temperature sensor in Celsius (°C)
high_temp_sec | How many seconds the temperature was HIGH since the last temperature status change (from normal to high) (initial value, when starting the engine = 0)
normal_temp_sec | How many seconds the temperature was NORMAL since the last temperature status change (from high to normal) (initial value, when starting the engine = 0)
Temperature from Temperature sensor | Integer number (temperature in Celsius °C)
Lamp indicator for high temperature | Lamp indicator will be ON in case of high coolant temperature (temp_cel > 120°C) Lamp indicator will be OFF in case of normal coolant temperature (temp_cel <= 120°C)
Input
Output
Internal signals
Lamp indicator for high temperature | By default, is OFF
Initial

## Slide 3
Clarification requests
Question | Feedback
How much time after the debouncing time to turn ON/OFF the lamp indicator? | 
What should happen if a high temperature is detected right after the engine is turned on. Should the debouncing time be skipped? | 
If temperature bounce around the 120°C (under and over 120°C) the lamp indicator, it will switch from one state (ON/OFF) to another (OFF/ON) too often. Make the temperature limit dynamic? Example: If the lamp is turned ON soon, and should be turned OFF again, the limit of the sensor should be 115°C. if the lamp is turned OFF soon, and should be turned ON again, the limit of the sensor should be 125°C. | 
If the coolant (first check) is cold when the engine is started, should there be a wait time (sec/min) before the next check. |